| USER’S MANUAL Charger 1000W |
| --- |
| Appendix |
| CAUTION: Input and output end wiring of charger please really lock on endson, avoid equipment got burned by contact impendence. |
| Placement of the Unit |
| Set up |
| Tower: Connect Utility and DC Plug |  | RT: Connect Utility and DC Plug |
| Parallel Connection |
| ◎Number of parallel unit is up to 4. ----- When connect 2 groups of Charger 1000W in parallel , please select UL 1015 16AWG line material or the equal line material for the charger line in parallel of input and output -----When connect 3 or 4 groups of Charger 1000W in parallel , please select UL 1015 14AWG line material or the equal line material for the charger line in parallel of input and output |
| Specifications |
| AC INPUT Input Voltage 160V-280V Current 4.6Arms Max. Freq. 50Hz/60Hz±10% Power Factor ＞0.85 DC OUTPUT Output Voltage 273Vdc ± 3Vdc (NO LOAD) DC Output Current 5.0A Max. Power Capacity 1000W Max. Efficiency ＞0.85 at full load Power Up Time ＜75ms Line Regulation ≦1%(No LOAD) Ripple Approximate ±5V Noise Approximate ±3V ENVIRONMENTAL Operation Temperature 0℃ ~ 40℃ Cooling Forced air ventilation by DC fan. Humidity 10% ~ 90% RH PHYSICAL Dimensions (WxLxH)mm 166.0 x 282.0 x 86.0 Net Weight (Kgs) 3.2 PS：Most greatly may parallel to 4000W ( the maximum input current: 18.4A， maximum charging current: 20.0A) |

# Text boxes

192321782001006